## Slide 1
ENTERPRISE NETWORK
INFRASTRUCTURE DESIGN
& IMPLEMENTATION
01
Group Members :
ola mohamed
Salah sleem
tarek diab
omar hussein
hassan khattab
Presented to : Dr Hussain Harb
Supervised by En Youssef Selim

## Slide 2
02
Objective
Build a secure, resilient, and efficient network infrastructure with departmental segmentation.
  Divided into departments: HR, Finance, IT, and Guest
  11 interconnected networks using OSPF
Key technologies used:
  VLANs for segmentation and security
  Wireless Network (WiFi)
  IP Telephony
  DHCP for automatic IP distribution
  PAT for internet access using one public IP
  SSH for secure remote management
Project Requirements

## Slide 3
03
Network Segmentation
& OSPF
  We have 11 different network
  Used OSPF as the dynamic routing protocol
Areas distributed as follows:
  Area 0: Backbone
  Area 1: Finance 192.168.0.0/24
  Area 2: Guest 192.168.5.0/24
  Area 3: HR 192.168.1.0/24
  Area 4: Meeting 192.168.4.0/24

## Slide 4
04
VLAN Configuration
Department VLAN ID
  Finance 10
  HR 20
  IT 30
  Guest 40
  Voice (IP Phones) 50
  Black (Security) 100
VLAN Purpose:
Logical segmentation
Reduces broadcast domains
Increases department-level security

## Slide 5
05
Wireless Network Setup
  Wireless Access Points deployed in all areas
  Devices: Smartphones, Laptops
  Security: WPA2/WPA3 encryption
  Separate SSIDs for employees and guests

## Slide 6
06
IP Telephony Integration
  Cisco 7960 IP Phones used across departments
  All switches support VoIP phones
  QoS enabled to minimize voice delays
  IP Phones receive addresses via DHCP
  Assigned to Voice VLAN (ID 50)

## Slide 7
07
PAT
(Port Address Translation)
  All internal devices access the internet via one public IP
  Configured on the main router
  PAT translates internal IPs to a single external IP
  Enhances security and conserves public IPs

## Slide 8
08
DHCP Setup
  Central DHCP Server distributes IPs automatically

## Slide 9
08
DHCP Setup
  The 192.168.4.0 is subnetting as following

## Slide 10
09
Secure Remote Access
(SSH)
  SSH enabled on all routers and switches
  Local Secure login credentials for routers:
  Username: admin
  Password: cisco12345
  Local Secure login credentials for switches:
  Username: sadmin
  Password: cisco12345
  Remote management over encrypted connection

## Slide 11
09
Secure Remote Access
(SSH)
  SSH enabled on all routers and switches
  Using Radius for authentication
  Secure login credentials for routers:
  Username: admin
  Password: cisco123455
  Remote management over encrypted connection

## Slide 12
10
LAN Security Measures
  802.1x authentication to prevent unauthorized access
  Port security
  DHCP snooping
  ARP inspection

## Slide 13
10
Project overview

## Slide 14
11
Future Security Enhancements
To improve network security in future phases, the following technologies can be implemented:
1. Next-Generation Firewall (NGFW):
  Deep packet inspection and application-level control
  Detects and blocks advanced threats (e.g. malware, intrusions)
  Can be placed at the edge of the network or between critical VLANs
2. Multi-Factor Authentication (MFA) for SSH & Admin Access:
  Adds extra layer of protection for administrative access
  Combines password + token/mobile confirmation

## Slide 15
12
THANK
YOU